## Slide 1: RFID Mapping & Localization
Danielle Fuller, Aaron Gillespie, Matt Greenlee, Matt Hannon, Priya Mishra
PDR

## Slide 2: Functional Block Diagram

## Slide 3: Functional Block Diagram

## Slide 4: UHF Readers
Speedway Revolution by Impinj
Operating Frequency: 865 - 956 MHz
Low level reader protocol
  Language: C++, C#
  Access to: Phase, RSSI
  Impinj RShell console
4 monostatic TNC ports
Price: ~$1,500
Mercury5 by Thingmagic
Operating Frequency: 902-928 MHz
Mercury API (Serial)
  Language: C, RQL
  Access to: Phase, RSSI
  TX/RX Power level control
Up to 4 bistatic ports (TNC)
Price: ~$1,400

## Slide 5: Microcontroller
  Details:
    Microcontroller: ATmega328
    14 Digital I/O
    Language: C and usage of open libraries
  Purpose:
    Interface with computer UHF reader application
    Control RF switches
Arduino Uno

## Slide 6: Feedback Network
  Components:
    UHF Reader
    Computer Application
    Arduino
    RF Switches controlling PCB trace lengths
  Methods for Localization:
    RSSI algorithm to help verify RF switching network results based on sum/delta network
    Innovative power interrogation schemes to determine vicinity
    Potential use of phase information for determining distance, velocity, and direction of tag
UHF Reader
Computer
Arduino
RF Switches/ Beam Steering
Localizing Network

## Slide 7: Functional Block Diagram
`

## Slide 8: Antennas
  Details:
    Linearly polarized
    Horizontal beam width: 75°
    Vertical beam width: 65°
    Size: 8.5” x 8.5”
    Frequency: 900 MHz
    Gain: 8 dBi
    Weight: .45 kg
    Price: $44.99 [ x3 = $134.97]
  Connections:
    Coaxial connection to UHF reader (Tx)
    Coaxial connection to switches (Rx)
Flat Patch Antennas by L-Com

## Slide 9: Homemade Patch Antenna (Backup Plan)
  Pros:
    Cost significantly less
    Greater margin for error
  Cons:
    Look less professional
    Large amount of research and trial/error needed
  Reasons for COTS:
    Learning curve too steep
    Want client to be able to duplicate product independently

## Slide 10: Functional Block Diagram
`

## Slide 11: Localization (2-Element Array)
  Direction from Reader:
    Goal: accurate within 15°
    Use of three LEDs to show direction from current location
    Accomplished using steering network (steering the null)
  Distance from Reader:
    Goal: accurate within 3 feet
    Will read up to 6 meters away
    Accomplished using RSSI information from reader and triangulation

## Slide 12: Determining Distance
Separation distance between antennas is known (~0.75λ)
RSSI is related to distance—strength is weaker from further distances, stronger when closer
Use two known values to triangulate tag
  Will require testing and calibration to verify read distance is accurate
  May not be possible since sum (+) signal is fed to reader, not the signals from receiving antennas
    Could use dynamic power altering as backup—cut power in half, and if signal disappears you know the tag is between the limit and the half-way mark
d separation
d right strength
d left strength
RFID tag
antenna left
antenna right
D tag

## Slide 13: Determining Direction
  Steer null for more precise resolution (vs. wide beam width)
  Use RSSI (Received Signal Strength Information) to verify phase information (phase says to left, RSSI should be stronger for left antenna)
  Hybrid coupler: two inputs (antennas), two outputs (+/Δ)
      If Δ is positive, tag is right of null
      If Δ is negative, tag is left of null
      If Δ is zero, tag is in line with null
    We currently can’t find a device that does this—alternate method is use of a summing network (summing amplifier?) for + and a 180° phase-shift of one antenna for Δ
      Advantages: Adding one trace would be simple; low cost, low real estate
      Disadvantages: Need another RF switch (~$125); summer is noisy

## Slide 14: Null Steering

## Slide 15: Switching Software Flow Chart

## Slide 16: Costs
[Honeywell budget is not set in stone—reader purchase has been approved, but other funding has yet to be decided.]

## Slide 17: Schedule

## Slide 18: Testing
  UHF Reader:
  Connect an antenna directly to the reader and locate a known tag, comparing results with known parameters
  Antennas:
      Hook up antennas to a spectrum analyzer to confirm patterns/strength
      Steering:
      Test traces by hooking to network analyzer to verify the correct phase shift occurs for each length; Still TBD for testing switches
      Localizing:
      Feed in known input signals from a function generator and verify appropriate output signals on an oscilloscope
      Overall system:
      Hook everything together, point at tag with known ID, distance and direction, compare results with actual values

## Slide 19: Risk Mitigation
  UHF Reader:
  Access to phase information not accessible  Use RSSI and algorithm to determine direction
  Reader can’t process sum/difference signals simultaneously  Do phase comparison externally before the reader by going straight to Arduino
  Unable to get the sum/difference unit to function  Use a summer and 180° phase shifting traces and two more switches
  Antennas:
      Receiver beam widths of 65° reduce accuracy  Rework steering network with (possibly) more traces to fine-tune
      Steering:
      Desired phase shifts not achieved with PCB traces  Use a phase-shifting IC
      Can’t get funding for evaluation boards  Design own circuitry
      Localizing:
  Reader won’t read tags because of a malfunction  Call company, get money back, and spend remainder of project on design of subsections and a theoretical complete system